## Slide 1: Heating Efficiency Enhancement in Household with integrated solar system
Final Presentation: Jan Dycke, Tim Eisele, Peiren Yang

## Slide 2: Team members
Jan Dycke (Resource Manager)
Tim Eisele (IT Manager)
Peiren Yang (Team Chef)

## Slide 3: Introduction
Energy consumption in German household
Chart: Energy Consumption in private household 2015 Germany
| Space Heating | Warm Water | Special Process Heating | Space Cooling | Special Process Cooling | Mechanical Energy | Information and Communication Technology | Lighting
 | 0.686 | 0.144 | 0.062 | 0.002 | 0.047 | 0.007 | 0.036 | 0.017

## Slide 4: Solar thermal heating system
Water Tank
Solar energy is renewable energy
System efficiency highly related to the weather conditions
Additional heating system is needed to complete the solution
Picture source: www.solar-energy-for-homes.com/build-solar-water-heater.html

## Slide 5: Gas heating system with integrated solar Panels
PEIREN YANG

## Slide 6: Heating system with natural gas
Water boiler controlled by thermostats
Hot water storage
  Insulated water tank
Hot water supplies for
  Heating circulation
  Bath & shower
  Drinking
Picture source: www.gas24.co.uk

## Slide 7: Heating solution with integrated solar system
Heated water is stored in
the same water tank
Gas heating works stable in
cloudy weather and night
Additional control logic for the
synergy of the two systems
Picture source: genesisenergysolutions.com

## Slide 8: Evaluation of the solution
Energy efficiency: 94% of industrial average
Installation cost: about 9,000 €
Running cost: about 844 € per year
CO2 Emission: about 8.6 tons per year
Prerequisites
  Central control system with thermostat
  Natural gas accessibility

## Slide 9: PELLET heating system with integrated solar heating system
TIM EISELE

## Slide 10: Pellet Heat – Pellet boiler
Water heated inside the boiler
Hot Water stored in tank
Not made for instant hot water delivery

## Slide 11: Pellet heat in combination with solar heat
Solar heating system adds 60°C water to the tank
Pellet heating system is on standby as long as tank temperature is sufficient
Instant hot water delivery is available until the capacity of the solar heating system is exhausted

## Slide 12: Pellet Heat – Solution Evaluation
Efficiency: 85%
Installation Costs: about 20,000€
Operational Costs: 1,173€ per year
CO2 Emissions: none, wood is considered CO2 neutral
Prerequisites: none

## Slide 13: Geothermal heating system with integrated solar heating system
JAN DYCKE

## Slide 14: Geothermal Heat – Downhole Heat Exchanger
Heat pump collects thermal Energy from the ground
Heats up warm water storage
The higher temperature difference, the lower heat pump efficiency
Ground (10° -15° C)
House
Heat Pump
Tank

## Slide 15: Geothermal Heat – Combination with Solar Heat
Solar system can heat warm drinking water (60°C) more efficiently
Geothermal system has no lead time
Solar overcapacities in summer can be used to regenerate the ground
Ground (10° -15° C)
House
Heat Pump
Tank
Solar Heat

## Slide 16: Geothermal Heat – Solution Evaluation
Efficiency: up to SPF of 6
Installation Costs: about 20,000€
Operational Costs: about 950€ per year
CO2 Emissions: none (eco tariff)
Prerequisites: suitable geological realities

## Slide 17: Evaluation and Recommendation
Criteria \ Solution | Gas Heating | Pellets Heating | Geothermal Heating
Efficiency | 0 | 0 | +++
Costs | ++ | + - | - 0
CO2 Emissions | - | 0 | +
Prerequisites | + | 0 | -
 | 3 x + 1 x - | 1 x + 1 x - | 4 x + 2 x -
In urban areas gas heating is the best solution
In suburban and rural areas geothermal heating is the best solution

## Slide 18
Q & A